## Slide 1: RPi 2/3, I2C, Analog Sensor
jyheo0@gmail.com

## Slide 2: I2C (I-squared-C)
Serial computer bus invented by Philips Semiconductor
Typically used for attaching lower-speed peripheral ICs to processors and microcontrollers
A sample schematic with one master (a microcontroller), three slave nodes (an ADC, a DAC, and a microcontroller), and pull-up resistors Rp
https://en.wikipedia.org/wiki/I%C2%B2C

## Slide 3: ADC, DAC
ADC - Analog to Digital Converter
DAC - Digital to Analog Converter
PCF8591t
  3 ADC, 1 DAC
  value range: 0~255
YL-40 board with PCF8591t
AOUT
AIN0
AIN1
AIN2
AIN3
SCL
SDA
GND
VCC
P4
P5
P6
Jumper P4 for AIN1: R6 thermister
Jumper P5 to AIN0: R7 photocell
Jumper P6 to AIN3: The single turn 10K ohm resistance
Removing a jumper allows an input channel to be fed from one of the external pins, labelled accordingly.

## Slide 4: Enable I2C in RPi
Enable I2C in raspi-config and reboot
$ sudo raspi-config
Interfacing Options 선택 > I2C 선택

## Slide 5: Enable I2C in RPi
Enable I2C in raspi-config and reboot
Check if the I2C kernel module is loaded
  $ lsmod
  i2c-dev, i2c-bcm???? must be listed!
Test
  $ i2cdetect -y 1

## Slide 6: Wiring RPi and YL-40
YL-40 | RPi
SCL | SCL1
SDA | SDA1
GND | GND
VCC | 3V3

## Slide 7: Photocell on YL-40
$ python3 yl40.py 0
import smbus
import time
import sys
bus = smbus.SMBus(1)
address = 0x48
if len(sys.argv) == 2:
i = int(sys.argv[1])
input_addr = 0x40 + i
else:
input_addr = 0x40
while True:
bus.write_byte(address, input_addr)
bus.read_byte(address)
aread = bus.read_byte(address)
print(aread)
time.sleep(0.2)
# AIN0 0x40: photocell
# AIN1 0x41: thermister
# AIN3 0x43: registance
https://github.com/jyheo/rpi2/blob/master/yl40.py

## Slide 8: Temperature Sensor - LM35
Wiring
  LM35 1 to RPi 3V3
  OUT to YL-40 AIN2
  GND to RPi GND
$ python3 yl40.py 2
https://github.com/jyheo/rpi2/blob/master/yl40.py

## Slide 9: Vibration Sensor
Wiring
  One leg of Vibration Sensor to RPi 3V3
  The other leg to YL-40 AIN2
$ python3 yl40.py 2
https://github.com/jyheo/rpi2/blob/master/yl40.py

## Slide 10: IR Receiver
Wiring
  Longer leg of Vibration Sensor to RPi 3V3
  The other leg to YL-40 AIN2
$ python3 yl40.py 2
IR Receiver can be used to detect motion
https://github.com/jyheo/rpi2/blob/master/yl40.py

## Slide 11: Analog OUT
$ python3 yl40w.py 255
  Turn on green LED of YL-40
$ python3 yl40w.py 0
  Turn off the LED
import smbus
import time
import sys
bus = smbus.SMBus(1)
address = 0x48
if len(sys.argv) == 2:
v = int(sys.argv[1])
bus.write_byte_data(address, 0x40, v)
else:
print(‘sudo python yl40w.py 0~255’)
https://github.com/jyheo/rpi2/blob/master/yl40w.py

## Slide 12: Exercise
Write a python program
  To display temperature and light
Motion detection LED
  Detect motion using IR receiver
  Once detecting motion, keep turning LED on for 3 seconds